## Slide 1
University Physics
Chapter 15 ALTERNATING-CURRENT CIRCUITS

## Slide 2: Learning Objectives
15.1 AC Sources
Introduction
15.2 Simple AC Circuits
Resistors, Capacitors, Inductors
15.3 AC RLC Series Circuits
Phasor Diagrams
15.4 Power in AC Circuits
RMS Power
15.5 Resonance
Q-Factor
15.6 Transformers

## Slide 3: Figure 15.3
Remember from Ch. 13 on Faraday’s Law we found that we can generate emf’s or voltages using rotating coils.
This is the basis of power generation for the transmission of electricity.
Devices that generate the power are typically sinusoidal, time-varying sources.
We call these Alternating Current (AC) sources.
Flow of charge reverses direction periodically… and therefore, so does the voltage...
Here in the USA typical electrical outlets provide a potential difference of 120 V at a frequency of 60 Hz.
  In other parts of the world: 220/240 V at 50Hz
Thus, the source voltage (or current) can be characterized by:
Where, V0 is the peak voltage.
15.1
15.1 AC SOURCES

## Slide 4: resistors
When we connect a resistor to an ac voltage source, we can use Ohm’s law to find the current flowing through the resistor:
Because in ac circuits the voltage and current can both be positive and negative, it is convenient to define the root mean square (rms) voltage or current:
The average squared voltage over one cycle:
Which defines the rms voltage:
And a similar equation for current.
15.2
15.2 SIMPLE AC CIRCUITS
peak current

## Slide 5: Figure 15.5
For the simple resistive circuit, we find that if the voltage has a sinusoidal dependence, the current has exactly the same time dependence.
In other words they are in phase with each other.
So, whenever the voltage is at its peak value, so to is the current.

## Slide 6: Figure 15.6
The phasor diagram representing the current through the resistor.
The phasor diagram representing both iR(t) and vR(t) .
phasor diagrams
We can represent the time-dependence of the voltage/current as a rotating vector (by virtue of its sinusoidal nature).
This is known as a phasor diagram.

## Slide 7
capacitors
We can extend the concept of phasor diagrams to other circuit components.
We will see differences between resistors, capacitors, and inductors.
For capacitors, remember the charge on a capacitor, Q = CV.
Now, for time-dependent voltages:
And current is the time-derivative of charge:
With, I0 = w C V0
Rewrite this as:
We can define an effective resistance associated with the capacitor through Ohm’s law:
15.3
capacitive reactance

## Slide 8: Figure 15.8
capacitor phasor diagram
Figure 15.7
A capacitor connected across an ac generator.
The current iC(t) through the capacitor and the voltage vC(t) across the capacitor. Notice that iC(t) leads vC(t) by 𝜋/2 rad.
The phasor diagram for the capacitor of Figure 15.7. The current phasor leads the voltage phasor by 𝜋/2 rad as they both rotate with the same angular frequency.

## Slide 9
inductors
Remember the voltage difference across an inductor:
So the current is obtained by integrating the voltage:
Giving,
With, I0 = - V0 / w L
Hence, Ohm’s Law yields:
15.7
inductive reactance
15.8

## Slide 10: Figure 15.10
inductor phasor diagram
Figure 15.9
An inductor connected across an ac generator.
The current iL(t) through the inductor and the voltage vL(t) across the inductor. Here iL(t) lags vL(t) by 𝜋/2 rad.
The phasor diagram for the inductor of Figure 15.9. The current phasor lags the voltage phasor by 𝜋/2 rad as they both rotate with the same angular frequency.

## Slide 11: resistors, capacitors, inductors in series
A circuit that contains a resistor (R), capacitor (C), and an inductor (L) is called a RLC circuit.
Using Kirchoff’s laws to sum the voltages across each element yields a 2nd order, differential equation:
This is the same as a damped, forced, harmonic oscillator.
15.3 RLC SERIES CIRCUIT
(differentiate)
Figure 15.11

## Slide 12: Figure 15.11
RLC Phasor diagram
Figure 15.12
Phasor diagrams offer an alternative method to analyze RLC circuits without having to solve a differential equation.
The results presented here correspond to the steady state.
CIVIL
Circuit Element | Relationship | Reactance X | Phase q | Angle Notation
Resistor | VR = I R | R | in phase | 
Capacitor | VC = I XC | XC = 1/wC | Leads +90o | 
Inductor | VL = I XL | XL = wL | Lags -90o | 

## Slide 13: Figure 15.13
The resultant of the phasors for vL(t) , vC(t), and vR(t) is equal to the phasor for v(t) = V0 sin ωt. The i(t) phasor (not shown) is aligned with the vR(t) phasor.
The resultant phasor of amplitude V0 is obtained as the vector sum of the individual phasor voltages:
Since VL and VC are colinear, we have:
The impedence, Z, is defined through:
And the phase angle between voltage and current:
impedence
15.10
15.11
15.9

## Slide 14: RLC CIRCUIT
Notice from the expression for the impedence for the RLC circuit, the current can become very large for certain values of the inductance and capacitance:
In particular, when XL = XC
This defines the resonant frequency w0:
RLC circuits were used in devices such as radios to pick out specific radio channels.
15.5 RESONANCE
15.17
Figure 15.18

## Slide 15
For ac circuits, We can find an expression for how the power varies with time using: P = IV
Since the power fluctuates, we consider the average power
15.4 POWER
Hence, the time-averaged power:
Which generalizes to:
Where,
15.13
15.14

## Slide 16
A stereo receiver applies a peak voltage of 40 V to a speaker. The speaker behaves approximately as if it had a resistance of 10 Ω.
Determine
40 V
10 Ω
10-Ω
Example: Electrical Power Sent to a Loudspeaker
(a) the rms voltage
(b) the rms current
(c) the average power for this circuit

## Slide 17: Figure 15.20
The rms voltage from a power plant eventually needs to be stepped down from 12 kV to 240 V so that it can be safely introduced into a home. A high-voltage transmission line allows a low current to be transmitted via a substation over long distances.
15.6 TRANSFORMERS

## Slide 18: transformers
A transformer is a device for increasing or decreasing an ac voltage.
The ac current in the primary coil creates a changing magnetic field that is fed by the iron core through the primary and secondary coils.
The resulting changing flux generates an induced emf in both the primary (self-inductance) and secondary coils (mutual-inductance).

## Slide 19: transformer equation
Applying Faraday’s law to both coils:
Now using the fact that the flux is (approximately) the same in both coils:
Finally, if the resistances in the coils are negligible, so the emfs are nearly equal to the terminal voltages, V:
Transformer equation
Ns> Np: larger secondary voltage  step-up transformer. Step-down transformer is opposite.
15.21
15.20

## Slide 20: power
Step-up transformer steps up the voltage & steps down the current.
Step-down transformer steps down the voltage & steps up the current.
The average power delivered to each coil, P =IV, is (approximately) the same (conservation of energy):

## Slide 21
Since, P = I2R, and resistance depends on the cross-sectional area of the wires, electricity is usually transmitted over long distances using thicker wires, higher voltages, and smaller currents in order to reduce the amount of power lost during transmission.

## Slide 22
Conceptual Example: Extension Cords and a Potential Fire Hazard
During the winter, many people use portable electric space heaters to keep warm. Sometimes, however, the heater must be located far from a 120-V wall receptacle, so an extension cord must be used. However, manufacturers often warn against using an extension cord. If one must be used, they recommend a certain wire gauge, or smaller. Why the warning, and why are smaller-gauge wires better then larger-gauge wires? (larger gauge wires have smaller cross-sectional area)